## Slide 1: PSH3D: A PetaScale Solver of the Helmholtz Equation in 3D
Darren Adams1 Michael Dodd2 & Antonino Ferrante2
1The National Center for Supercomputing Applications
University of Illinois
2William E. Boeing Department of Aeronautics & Astronautics
University of Washington

## Slide 2: Motivation: High Reynolds-Number DNS Applications
Study of “turbulence in a box” – Isotropic periodic boundary conditions
  Universality of statistics in inertial range.
  Statistical dependence on Reynold number and scale
Turbulent boundary layer (Wall Flows)
Droplet-Laden Flow
High resolution and high Reynolds numbers require Petascale supercomputers and beyond.

## Slide 3: Goals of the UW-XSEDE ECSS Collaboration
Adapt an existing parallel 1D decomposition (1DD) DNS code, capable of running on proc., to enable Petascale ( proc.) runs on much larger grids.
Keep existing numerical approach, if possible, but move to 2D decomposition (2DD).
  Many established use cases, good performance.
  Allows Neumann, Dirichlet and shear-periodic B.C. without affecting performance.
  Can compare 2DD results to 1DD runs for verification.
Focus on Poisson (Helmholtz) solver: Main bottleneck of pressure-correction step in DNS code.

## Slide 4: 3D Helmholtz Equation on Cartesian Mesh With Periodic Boundary Conditions
General 3D Helmholtz Eq:
Discrete (central finite difference) form:
Periodic BC on x and y:
Shear-periodic BC along z:

## Slide 5: Numerical Approach
Combining a 2D Fourier Transform of source terms:
…with 2D inverse Fourier transform of the solution:
With:

## Slide 6: Numerical Approach
where:
And boundary conditions
Results in a linear system along the z-dimension…

## Slide 7: Linear System is Tri-Diagonal with Periodic B.C.

## Slide 8: Summary of Numerical Method
2D FFT (along x, then y) on source terms.
  R2C transform along x for every (j,k)
  Complex DFT along y for every (i,k)
Solve complex tri-diagonal linear system along z for every (i,j).
Inverse 2D FFT (along y,then x)
  Complex backward DFT along y for every (i,k).
  C2R backward transform along x for every (j,k).

## Slide 9: One Dimensional Decomposition (1DD)
Domains split along y-dimension; global in x and z.
Efficient Scaling – Only one parallel dimension.
Limited Scaling to No. of Domains in a single grid direction.
Not sufficient to reach PetaScale.

## Slide 10: Parallel 2D FFT
Perform FFT on global x-dimension using serial FFTW (http://fftw.org) routine for each (j,k)
Perform Global transpose using MPI_Alltoall; data is now split along x-dimension and global in x and z.
Perform FFT on y-dimension for each (i,k)

## Slide 11: Two Dimensional Decomposition(2DD)
(Practically) unlimited Scaling
  Max NP ~ (Nz)(Ny)
2 parallel dimensions means: more complexity .
Common approach is to use 3D FFT which requires a minimum of 4 global transpose operations.
Combine Parallel 2D FFT with parallel linear solver
Same parallel 2D FFT from 1DD can be used independently on each y sub-communicator.
No need for 2nd set of global transposes as with 3D FFT.

## Slide 12: Construction of Parallel Linear Solver Schumann and Strietzel (1995)
Use solutions to a localized problem:
And a localized homogenous problem (that is independent of the R.H.S.):

## Slide 13: Construction of Parallel Linear Solver (PLS)
…to construct a final solution:
with the requirement:
producing a reduced linear system:
where
and
With B.C.:

## Slide 14: Linear System for R-amplitudes is same form as The Global System
Same tri-diagonal periodic form as global linear system =>
Re-use the existing serial Linear Solver once R-values are Gathered.

## Slide 15: Overview of Parallel Linear Solver
Initialize and store values that are independent of the R.H.S: such as and
Compute localized solutions and local .
  Requires nearest-neighbor communication of R.H.S. values; scales very well
Do global reduction to correct solutions at the domain boundaries; does not scale well
  Uses Same linear solver as serial problem, with a smaller set of inputs and modified R.H.S.
Compute final solution
  Requires nearest neighbor exchange of -values.
  scales very well

## Slide 16: Overview of 2DD Parallel H3D Solver
Execute Forward R2C FFT along x-dimension.
Perform Transpose (x,z,y) array -> (y,z,x)
Execute Forward DFT FFT along y-dimension
Execute Parallel linear solver along z-dimension
Execute inverse DFT FFT along y
Perform Transpose (y,z,x) -> (x,z,y)
Execute Backward C2R FFT along x.

## Slide 17: Method Breakdown on Stampede 16384 cores

## Slide 18: Strategies to Reduce Cost of Global Reduction
Use bulk MPI operations: MPI_Gather MPI_Scatter on entire (j,i) set of k-vectors to gather/scatter R-values.
“Multi-level” parallel decomposition “Distributed Gather”
  Exploit the independent nature of linear systems.
  Use all available processors to work on subsets of (j,i) index space; Each k-rank gathers and scatters.
Use MPI-3 non-blocking Collectives: MPI_IGather, MPI_Iscatter to further optimize global data operations. This allows individual chunks of R-values from each k-rank to “fly” simultaneously.

## Slide 19: Global Reduction of “R”-values. “Root-Gather” vs. “Distributed-Gather”

## Slide 20: MPI-3 Non-Blocking Communication
do k = 0,this%ndomk – 1
offset = 1+k*this%JL(1)
call mpi_igather(….,…,ier)
enddo
Call mpi_waitall(this%ndomk,req,MPI_STATUSES_IGNORE,ier)
Allows all gather (and subsequently scatter) requests to be posted concurrently.
Since the operations occur on distinct processor groups (MPI sub-communicators), the overall bandwidth should increase.

## Slide 21: Distributed Gather and MPI-3 non-blocking collectives optimizations

## Slide 22: Performance on BlueWaters Grid; (Strong Scaling)
Start with 3D-FFT Method using P3DFFT (D. Pekurovsky SDSC) as a comparison. How does the Parallel Linear Solver Approach scale and perform compared to a 3D FFT which requires 4 global transpose operations?
Initial implementation with “Root-Gather” shows similar performance to 3D FFT
Optimized implementation with “distributed-gather” and MPI-3 non-blocking collectives. Shows improved performance.
Comparison to optimal “No Global” version of solver for a diagonally dominant linear system.

## Slide 23: “Partial Global” Optimization
Is it possible to avoid the global reduction for some of the linear systems; those that are to some degree diagonally dominant?
Will the solution accuracy be acceptable?
If so, will this push performance closer to the “No-Global”?
Complicated implementation: requires non-contiguous data access via MPI_TYPE_INDEXED

## Slide 24: Magnitude of from 2D FFT in x-y Plane
Diagonal Dominance
The diagonal terms of the linear systems for each (i,j) are proportional to the Fourier mode components:

## Slide 25: “Partial-Global” Performance(BlueWaters)

## Slide 26
Timing Breakdown of various processor configurations
550 billion grid points)
131,072 ranks ().
The all-global PLS method (top) consistently deteriorates with increased ranks along z-dimension.
The partial global method mitigates the performance tail-off of the PLS and allows more efficient 2D FFTs to improve overall performance.
All-Global (Top) Partial Global (bottom)

## Slide 27: Summary
  The 2D FFT/PLS approach to solving the Helmholtz/Poisson eq. can scale well into the PetaScale Regime.
    Consistent performance advantage over 3D FFT approach.
    Works well with structured mesh applications such as DNS.
  Bulk MPI operations and distributed treatment of global reduction step are keys to unlocking performance.
    This approach is more efficient when MPI-3 non-blocking collective support is available.
  Skipping global reduction for diagonally dominant vectors can allow very fast solution times (approaching no-global case) for applications where the resulting errors are acceptable.

## Slide 28: Acknowledgements
Antonino Ferrante, NSF CAREER Award, grant number OCI-1054591.
Hyak, high-performance computer cluster at the University of Washington (UW).
Extreme Science and Engineering Discovery Environment (XSEDE), NSF grant number ACI-1053575.
XSEDE Extended Collaborative Support Service (ECSS) program
Blue Waters sustained-Petascale computing project, NSF (awards OCI-0725070 and ACI-1238993) and the state of Illinois.